UV Measurements on General Lighting and UV Application Lamps

Rolf S. Bergman

Rolf Bergman Consulting

# Abstract

Spectral irradiance measurements in the UV and visible region (200 – 800 nm) are presented for a number of different lamps including incandescent, halogen, fluorescent, and HID sources.  Some of these lamps are intended for general lighting where the design guide is to keep the UV output low enough so that the lamps can be considered exempt with respect to the exposure level guidelines provided by IESNA RP 27.1 (also CIE S009:2002).  UV emission from the source, i.e., filament or gas, may be modified by the choice of envelope material and/or coating used in lamp construction.  Here materials that effectively reduce both the UV output which affects photobiological safety and those that dramatically reduce the total UV emissions will be discussed.  Also it will be shown that for lamps containing a tungsten filament source the amount of UV transmitted through a UV transparent envelope material is a function only of the filament color temperature.

For specialty lamps, which are often very similar in design to the general lighting lamps, the idea is to produce significant UV emission in some wavelength region to accomplish given objectives.  The spectral output of Germicidal and Black light lamps are examples that will be discussed.  Limitations on exposure to these kind of lamps will also be discussed.

# Biography of Rolf S. Bergman

Dr. Rolf Bergman spent 28 years at GE Lighting in Cleveland before retiring in 2001 to set up a sole-proprietor business, Rolf Bergman Consulting.  After retiring from GE Dr. Bergman, in addition to working for pay, has involved himself in many technical volunteer activities.  He is currently the President of the US National Committee of the CIE.  He also is a member of the IESNA Photobiology Committee and the Technical Procedures Committee (TPC) and serves on the Technical Advisory Group for EPRI’s Lighting Research Office.

For most of his time at GE Dr. Bergman worked in a number of areas within the sphere of lamp research and development, achieving the title Chief Scientist.  In his later years he was responsible for the technical development of lamp measurement equipment and measurement processes.  He was also helped manage GE Lightings involvement in industry standards organizations such as ANSI and IEC.  He chaired technical committee, TC6-47 of the CIE, whose goal was to create a global standard for Photobiological Safety of Lamps and Lamp Systems, patterned after the RP-27 series.  CIE Standard S009:2002 is the result.

Dr. Bergman received his education at the University of Minnesota, graduating with a Ph.D. in Electrical Engineering in 1972.

He is married to Martha (Marty), nee Ott.  They have one son Douglas, an Assistant Professor at the Physics Department of Rutgers University, NJ.  Dr Bergman is also active in Church of the Saviour, United Methodist.